## Slide 1: FIR Workbook (lab_3)
SOC Design

## Slide 2: Function specification
Same as course-lab_2(FIRN11stream)
y[t] = Σ (h[i] * x[t - i])

## Slide 3: Design specification
TBD – Based on size of data file

## Slide 4: Deliver module header
The I/O signals are listed in fir.v.
You are requested to use simplified AXI-lite and AXI-stream protocol.

## Slide 5: Configuration Register Address map
0x00 – [0] - ap_start -> set when ap_start signal asserts
-> reset, when start data transfer, i.e. 1st axi- stream data come in
[1] – ap_done -> when FIR process all the dataset, i.e. receive tlast, and last Y is generated
[2] – ap_idle -> indicate FIR is actively processing data
0x10-14 - data-length
0x20-FF – Tap parameters,e.g 0x20-24 Tap0, in sequence …

## Slide 6: FIR module interface
For your reference:
  AXI-lite:
    https://www.realdigital.org/doc/a9fee931f7a172423e1ba73f66ca4081
    https://docs.xilinx.com/r/en-US/pg202-mipi-dphy/AXI4-Lite-Interface
  AXI-stream:
    https://developer.arm.com/documentation/ihi0051/latest/
    https://docs.xilinx.com/r/en-US/pg256-sdfec-integrated-block/AXI4-Stream-Interface

## Slide 7: Testbench
fir_tb(Please name your top module same as fir for simulation)
The testbench should keep in the same directory with Makefile
Block-level Protocol (ap_start, ap_done):

## Slide 8: Test dataset
Samples_triangular_wave.dat
out_gold.dat

## Slide 9: Submission (1/2)
Hierarchy:
  StudentID_lab3/
    Waveform
    Simulation.log
    Report.pdf
    Synthesis report
    Github link
Your Github link should attach the file
  Design, Synthesis report(Including FF, LUT, Bram ), Waveform, simulation.log, makefile,…etc.
  Report
Location of design (If use vivado to design)
  hostproject/hostproject.srcs/sources_1/new/

## Slide 10: What is included in the report
Block Diagram
  Datapath – dataflow
  Control signals
Describe operation, e.g.
  How to receive data-in and tap parameters and place into SRAM
  How to access shiftram and tapRAM to do computation
  How ap_done is generated.
  …..
Resource usage: including FF, LUT, BRAM
Timing Report
  Try to synthesize the design with maximum frequency
  Report timing on longest path, slack
Simulation Waveform, show
  Coefficient program, and read back
  Data-in stream-in
  Data-out stream-out
  Bram access control
  FSM

## Slide 11: Submission (2/2)
Compress all above files in a single zip file named
  StudentID_lab3.zip (e.g., 111061545_lab3.zip)
Submit to NTHU eeclass
Deadline:
  ‐ 20% off for the late submission penalty within 3 days